## Slide 1: Responsible sourcing of rare earth elements
Camborne School of Mines (University of Exeter)
Robert Pell
Resource scarcity workshop, East Kazakhstan
State Technical University

## Slide 2
Rare earth element applications
Figure 1. Proportional value of REO consumed by various industries from 2011-2014 (Industrial Minerals Company of Australia, 2014)
‘Quantifying the environmental performance of rare earth production using life cycle assessments’
Notes: REE distributed widely across the world
Difficult to extract and purify

## Slide 3: Life Cycle Assessment
A Life Cycle Assessment allows a quantitative assessment of the environmental performance of a product or process over its entire life cycle
Figure 2. Life cycle assessment framework (GaBi 6.0 , 2015)
Figure 3. Simplification of flows in and out of a rare earth element production process

## Slide 4
Processes and flowsheet at Bear Lodge
Processes and flowsheet at Mountain Pass
Mining
Crushing &
grinding
Chemical
beneficiation
Cracking &
separation

## Slide 5
Chart: 
| Total | Cracking & Separation | Chemical Beneficiation | Crushing & Grinding | Mining
Mountain Pass | 74.829 | 13.349 | 44.5 | 8.79 | 8.19
Bear Lodge (1-9) | 65.4451 | 43.8698 | 11.2 | 2.6953 | 7.68
Bear Lodge (10-45) | 80.2175 | 50.89 | 11.6 | 9.8475 | 7.88
Energy contribution (MJ/kg REO) during the production of REOs at Mountain Pass and Bear Lodge during phase 1 and 2 of development
Figure 4. Energy use in production of REOs (MJ/kg REO) at Mountain Pass and Bear Lodge
22.29%
Percentage of total energy consumed
during flotation at Mountain Pass
65.44
80.22
70.88
MJ/kg REO at Bear Lodge (yrs 1-9)
MJ/kg REO at Bear Lodge (yrs 10-45)
MJ/kg REO at Mountain Pass